## Slide 1
SRET-Based Calibration for EEG Neurofeedback
Using Self-Referential Encoding Task as a DMN Localizer for EEG-Only Calibration
rtBPD pilot (n=2) • DMNELF group model • DWT+stats features
June 2026

## Slide 2
Why SRET for Calibration?
Problem: calibrating the EEG decoder requires knowing what the fMRI network
state should be — but in EEG-only NF we don't have fMRI.
Previous calibration approaches:
• Feedback pseudo-target (baseline → feedback step): weak, hurts on rtBPD
• Rest calibration: hurts arousal-free targets (trains on arousal)
SRET advantage: a task with KNOWN DMN activation pattern
• Self-referential blocks → maximal DMN engagement
• Semantic control blocks → DMN suppression (external attention)
• Multiple self/semantic alternations per run → rich training signal
• Separate task from feedback → no feedback runs sacrificed
Literature supports (Cerebral Cortex 2017, Frontiers 2013):
DMN hierarchy: self > other > semantic/rest
Self-referential processing activates vmPFC, PCC — core DMN nodes
Semantic control (syllable counting) deactivates DMN

## Slide 3
Three SRET Contrasts Tested
Each contrast defines a different pseudo-target from the SRET block design,
convolved with the HRF:
Contrast A: Self vs Rest
self = +1.0, other = +0.5, semantic = 0, rest = 0
Simple: DMN on during self/other, off during rest
Contrast B: Self vs Semantic ★ (DMN localizer)
self = +1.0, other = 0, semantic = -1.0, rest = 0
Bipolar: DMN maximally ON (self) vs maximally OFF (semantic)
Most informative — model learns both DMN activation AND suppression
Contrast C: Graded
self = +1.0, other = +0.5, semantic = -0.5, rest = 0
Intermediate: uses all conditions at different levels
Each tested with 1 SRET run (~6 min) and all 4 SRET runs (~24 min)

## Slide 4
Results: SRET Calibration vs Alternatives
GSR'd CEN (n=2, rtbpd002 + rtbpd004):
Strategy mean r 002 004
─────────────────────────────────────────────────────────
SRET self vs semantic (1 run) ★ +0.092 +0.24 -0.05
SRET self vs rest (all runs) +0.092 +0.22 -0.04
SRET self vs semantic (all) +0.091 +0.20 -0.02
SRET graded (all) +0.088 +0.21 -0.03
No calibration (group only) +0.075 +0.17 +0.06
Feedback 1-run cal +0.044 +0.26 -0.00
PDA:
SRET self vs semantic (1 run) ★ +0.097 +0.26 -0.07
No calibration +0.096 +0.27 -0.00
SRET self vs rest (1 run) +0.083 +0.26 -0.09
Feedback 1-run cal +0.082 +0.28 -0.07

## Slide 5
Key Findings
1. SRET self-vs-semantic is the best calibration contrast
→ The bipolar DMN on/off contrast provides the richest training signal
→ Matches the published DMN localizer contrast
2. 1 SRET run (~6 min) is sufficient — no benefit from 4 runs
→ Practical for clinical deployment: short calibration task
3. SRET calibration improves GSR CEN over no-cal (+23%, 0.092 vs 0.075)
→ Does NOT hurt (unlike feedback cal which dropped to 0.044)
→ SRET is a safe calibration — worst case it matches no-cal
4. rtbpd002 benefits substantially from SRET cal (GSR CEN: 0.17 → 0.24)
rtbpd004 is a non-responder regardless of strategy
5. Recommended pipeline:
Group DWT+stats model → 1 SRET run calibration (self vs semantic)
→ Predict all feedback runs — no fMRI, no feedback sacrifice

## Slide 6
Recommended EEG-Only NF Pipeline
1. Train group model on EEG-fMRI cohort (DMNELF n=17)
DWT db4 statistical features (620f) + Ridge α=1000
2. New participant: run 1 SRET scan (~6 min, EEG only)
Self-referential vs semantic control blocks
Build pseudo-target: self = +1, semantic = -1, HRF convolved
Fit calibration Ridge on SRET EEG → pseudo-target
3. Deploy calibrated model for real-time CEN/PDA feedback
All feedback runs available — no runs sacrificed for calibration
Expected: GSR CEN r ≈ 0.09-0.24 depending on individual
No fMRI needed at any point for the new participant