## Slide 1
EEG Finger-Print (EFP) for DMN / CEN / PDA
Replicating Meir-Hasson et al. 2014 on the DMNELF simultaneous EEG–fMRI cohort
Single electrode · Stockwell time-frequency · data-driven bands · sliding-delay ridge · n=17

## Slide 2
The EFP method (what makes it different)
• Single electrode (data-driven best, by validation NMSE) — not multivariate.
• Stockwell (S-)transform time-frequency at 1 Hz (implemented from scratch, FFT-based).
• 10 data-driven equal-energy frequency bands (not fixed delta/theta/alpha).
• KEY: a [frequency × sliding time-delay] design (0..−12 s) → ridge learns a SEPARATE delay for each frequency. No assumed HRF shape.
• Double cross-validation: outer m-k-fold block CV (k=5,m=2) + inner RidgeCV for λ.
• Baselines on same folds: Theta/Alpha ratio (traditional) and fixed-HRF predictor.
• Built at both native-TR and 4 Hz-upsampled resolution to test the paper's up-sampling claim.

## Slide 3
Within-subject: EFP beats both baselines (EFP ≥ HRF ≥ T/A)
• Replicates the paper's ordering across every target; strongest for CEN, PDA, GSR_CEN, GSR_PDA (r≈0.25–0.28). GSR_DMN weakest (r≈0.11–0.17), consistent with our other pipelines.

## Slide 4
Interpretable fingerprints — a learned HRF per frequency
• Group-averaged [band × delay] EFP. Weights peak at ~−4 to −7 s delay — an HRF-plausible lag learned data-drivenly, differing across frequency bands.

## Slide 5
EFP vs our prior methods — a clear improvement
• Within-subject EFP roughly doubles PDA decoding (r=0.26 vs DWT 0.11, HMM 0.10) and improves GSR_CEN (0.26 vs 0.17).
• Even cross-subject (LOSO) EFP transfers for PDA (r=0.13, p=0.01) — a general fingerprint.

## Slide 6
Cross-subject generalization & TR vs 4 Hz
• LOSO general fingerprint (train N−1, predict held-out), TR resolution:
  – PDA: r=+0.127 (p=0.010, ch Pz)
  – CEN: r=+0.084 (p=0.001)
  – DMN: r=+0.066 (p=0.002)
  – GSR'd targets transfer weakly across subjects (p>0.05) — GSR removes shared signal.
• TR vs 4 Hz up-sampling: comparable within-subject accuracy — confirms the paper's finding that up-sampling adds temporal detail but not correlation.

## Slide 7
Paper-style figures I — EFP fingerprints
Meir-Hasson Fig 5c/7c analog: [frequency × time-delay] per target

## Slide 8
Paper-style figures II — predictor overlay & electrode topography
Fig 3d (predictor vs fMRI) and Fig 3e/5b (per-electrode CV correlation r; red=better)

## Slide 9
Paper-style figures III — post-processing (Fig 2 analog)
EEG → S-transform → 4 Hz → data-driven bands → band-averaged TF → sliding window; fMRI ROI → 4 Hz + normalized

## Slide 10
Paper-style figures IV — prediction I/O, PDA (Fig 3 analog)
a) ROI signal + ROI mask b) bottom/top-25% EEG TF c) EFP d) predictor vs fMRI e) per-electrode r

## Slide 11
Paper-style figures IV — prediction I/O, CEN (Fig 3 analog)
a) ROI signal + ROI mask b) bottom/top-25% EEG TF c) EFP d) predictor vs fMRI e) per-electrode r

## Slide 12
Paper-style figures IV — prediction I/O, GSR_CEN (Fig 3 analog)
a) ROI signal + ROI mask b) bottom/top-25% EEG TF c) EFP d) predictor vs fMRI e) per-electrode r

## Slide 13
Positive control — visual cortex (Fig 5 analog)
Focal 6mm calcarine sphere (MNI -1,-86,13 ~ V1). Blind EFP localizes posteriorly (group-mean peak Pz; LOSO best O2) with alpha modulation — recovers occipital topography, validating the method

## Slide 14
Verdict
• Faithful EFP replication succeeds on DMNELF.
  – The sliding-delay single-electrode fingerprint is our best DMN/CEN/PDA decoder to date, within-subject (PDA r≈0.26, CEN r≈0.28).
  – A general (LOSO) PDA fingerprint transfers across subjects (r≈0.13, p=0.01) — promising for EEG-only neurofeedback.
  – Interpretable [freq × delay] fingerprints show HRF-plausible per-frequency delays — good paper figures.
• Caveats
  – GSR_DMN remains hard (within and across subjects).
  – LOSO uses band-index alignment across per-subject data-driven bands (approximation); a fixed-band group model is the natural next step.