## Slide 1
Multivariate EEG Band Power → fMRI Network Decoding
Decoding DMN and CEN from simultaneous EEG
16 subjects • simultaneous EEG-fMRI • neurofeedback task
DMNELF Project • June 2026

## Slide 2
The Goal
Decode fMRI network activity (DMN, CEN) from simultaneous EEG
Why? So EEG alone can drive real-time neurofeedback without the MRI scanner
Data:
• 16 subjects, simultaneous EEG-fMRI
• 4 runs × 125 TRs (TR = 1.2s), neurofeedback task
• 31 EEG channels (10-20), preprocessed at 500 Hz
• fMRI: personalized DMN and CEN ROI timeseries

## Slide 3
Methods Overview

## Slide 4
Step 1 — EEG Feature Extraction: Hilbert Envelope
For each TR (1.2s), compute power in 5 bands per channel:
δ (1–4) θ (4–8) α (8–13) β (13–30) γ (30–40 Hz)
1. Bandpass filter → isolate each band
2. Hilbert transform → analytic signal
3. |analytic| = instantaneous amplitude envelope
4. Average per TR → log transform
Result: 31 channels × 5 bands = 155 features / TR
Why Hilbert over FFT?
Preserves temporal dynamics at the TR timescale

## Slide 5
Step 2 — HRF Convolution
EEG is instantaneous, BOLD is delayed ~6s
Convolve EEG band power with the canonical
hemodynamic response function (HRF):
• Double-gamma model, 32s duration
• Peak at ~6s (main response)
• Undershoot at ~16s
This temporally aligns EEG features with
the fMRI signal they should predict

## Slide 6
Step 3 — Common Average Re-referencing (CAR)
At each TR, subtract the spatial mean across 31 channels within each band
Removes the global broadband EEG component (= arousal) from the predictor side (X)

## Slide 7
Step 4 — fMRI Targets & Global Signal Regression
Four targets (z-scored per run):
RAW DMN — includes arousal (sanity check)
GSR'd DMN — arousal removed
GSR'd CEN — arousal removed
PDA (CEN − DMN) — intrinsically arousal-free
GSR removes arousal from the target side (y):
DMN(t) = β₀ + β₁ × global_signal(t) + residual
Keep only the residual
DMN loads on global signal at r ≈ 0.70
→ ~50% of DMN variance is just arousal
CAR (EEG) + GSR (fMRI) = arousal removed
from both sides of the equation

## Slide 8
Step 5 — Ridge vs ElasticNet Regression
Both: linear regression + regularization penalty
(prevents overfitting with 155 correlated features)
Ridge (L2): penalty = Σ weight²
• Shrinks all weights toward zero
• Never sets any to exactly zero
• "Use everything, trust nothing too much"
ElasticNet (L1 + L2): penalty = mix of |weight| + weight²
• L1 can push weights to exactly zero → feature selection
• L2 handles correlated features gracefully
• Sparser, more interpretable model
ElasticNet won: zeroed only 6% of features
→ confirms the signal is genuinely distributed
but pruning noise improved generalization

## Slide 9
Step 5 — Cross-Validation Schemes
No shuffle — contiguous blocks preserve temporal autocorrelation (shuffled KFold gives spurious r = 0.5–0.75)

## Slide 10
Step 6 — Statistical Testing (Permutation Nulls)
No parametric assumptions — pure permutation tests:
Per-subject: circular-shift null (10K)
• Shift fMRI target by random lag within each run
• Preserves autocorrelation structure
• Refit model → null r distribution
• p = fraction of null r ≥ observed r
Group: sign-flip null (10K)
• Randomly flip sign of each subject's mean r
• Compute null group mean
• Tests cohort-level effect
Both are non-parametric, FWER-controlled

## Slide 11
Step A — Univariate Screen: It's All Arousal
Raw EEG band power couples to DMN at r ≈ 0.30
→ pipeline is sound (alignment, HRF, artifacts OK)
BUT: coupling is 100% arousal/vigilance:
• Uniform across ALL channels and bands
• Tracks fMRI global signal at r ≈ 0.45
• Collapses to r = 0 after partialling global signal
• = aperiodic 1/f broadband shift, not oscillatory
After CAR or GSR:
nothing survives group correction
→ Dead end for univariate (single channel) decoding
→ Need multivariate approach (Step B)

## Slide 12
Step B — Multivariate Decoder: POSITIVE RESULT

## Slide 13
Per-Subject Decoding Performance

## Slide 14
Cross-Run Generalization (5-fold vs LORO)
Signal holds across runs — not just within-run autocorrelation leakage

## Slide 15
ElasticNet Weight Topography — GSR'd CEN

## Slide 16
Top Features: What Drives the Decoder?

## Slide 17
EEG-Predicted vs True fMRI (Best & Worst Subject)

## Slide 18
EEG-Predicted vs True fMRI (Best & Worst Subject)

## Slide 19
ElasticNet Weight Matrix (Group Mean, GSR'd CEN)
Key findings:
• F4 alpha is the single most reliable feature
(right-frontal alpha → CEN, 13/16 agree)
• Consistent with frontal alpha
asymmetry literature
• Signal is distributed and broadband
— no single band or region dominates
• Only 6% of weights zeroed out
→ truly distributed, not sparse
• Good cross-subject consistency
(10–14/16 subjects agree on sign)

## Slide 20
Bottom Line
There IS a network-specific EEG signature of DMN/CEN activity beyond arousal
But it is a distributed multivariate pattern — no single electrode or frequency band carries it
ElasticNet on HRF-convolved, CAR'd band power reliably decodes it within and across runs
GSR'd CEN is the most decodable target: r = +0.21 (p = 0.0006)
F4 alpha (right-frontal) is the top feature — consistent with frontal alpha asymmetry literature

## Slide 21
Next Steps
Step C — Microstates / Connectivity
EEG microstates C/D ↔ DMN; alpha connectivity instead of power
May capture complementary signal to band power
Step D — Slow-State Classification
Classify high-DMN vs high-CEN windows instead of continuous regression
May be more robust with the distributed pattern
Real-time application
Train on calibration runs → predict in real-time with EEG only
LORO r = 0.16 for GSR'd CEN suggests this is feasible